## Slide 1: SOCKET COMMUNICATION USING AT+QIOPEN/AT+QISEND FOR TCP MODULES OF CAVLI

## Slide 2: SOCKET COMMUNICATION
A socket is an endpoint for sending or receiving data across a network.
Socket communication allows two devices to exchange data over protocols like TCP or UDP.
TCP (Transmission Control Protocol) is reliable and connection-oriented.
Commonly used in IoT for transmitting sensor data, commands, or updates.
AT commands like AT+QIOPEN & AT+QISEND allow embedded modules to open sockets and send data.

## Slide 3: CAVLI TCP MODULES
Cavli Modules that support TCP/IP communication include: C16QS, C10GS, C42QM.
Network support 2G, 3G, 4G.
Features include TCP/IP over AT commands.
Interfaces available: UART, USB, GPIO, ADC, I2C (depends on module).

## Slide 4: Cavli modules like C16QS use these AT commands for socket operations:
AT+QIOPEN – Opens TCP/UDP socket.
AT+QISEND – Sends data over socket.
AT+QICLOSE – Closes socket connection.

## Slide 5: AT COMMAND FLOW FOR SOCKET COMMUNICATION
1. Configure GPRS Connection
AT+QIFGCNT=0 → Select bearer profile
AT+QICSGP=1,"your.apn.here" → Set APN2.
2. Connect to Internet
AT+QIREGAPP → Register to GPRS
AT+QIACT → Activate PDP context
3. Open and Use Socket
AT+QIOPEN="TCP","your.server.com",80 → Open socket
AT+QISEND → Send data like
AT+QICLOSE → Close connection

## Slide 6: Applications:
IoT telemetry transmission
Remote equipment control
Sending data from embedded sensors to the cloud